## Slide 1: Forecasting the CLEAR beam charge
AISSAI ACCELERATOR HACKATHON 2026
OPTIMISATION CHALLENGE
How will the beam behave next, and can we see it coming?
Antonio Gilardi
CERN · CLEAR · antonio.gilardi@cern.ch
past shots
dropout
now
forecast
Notes: Welcome. This is the forecasting part of the optimisation challenge, on real data from CLEAR at CERN. The picture is the whole story: the beam charge jitters and drifts shot by shot, sometimes drops out, and the question is whether we can see where it goes next.

## Slide 2: Users need a stable charge
WHY
The dose and the detector signal scale with the beam charge.
WHAT USERS NEED: A STEADY CHARGE
WHAT THE MACHINE GIVES: DRIFT, JITTER, DROPOUTS
THE CAUSES ARE EVERYWHERE
Laser · power and cathode spot
RF · amplitudes and phases
Ambient · temperature, humidity
No single knob fixes it.
Forecasting the CLEAR beam charge
02
Notes: Many CLEAR users need the charge to stay stable, because what they measure scales with it. Medical irradiation alone is 43 % of CLEAR's experiments. Top: what users would like, a charge that stays inside its tolerance. Bottom: what the machine actually gives, drift over time, shot-to-shot jitter and sudden dropouts. The causes are spread across the machine, the laser, the RF, even the hall temperature, and there is no single knob to turn.

## Slide 3: CLEAR at a glance
THE MACHINE
Laser
Hits the photocathode. The camera BTV0125 sees its spot.
RF gun
Accelerates the electrons. BCM_GUN reads the charge.
Accelerating structures
Fed by 2 klystrons: MKS11, MKS15.
Experimental areas
Medical, plasma lens, in-air, VESPER.
Coloured boxes: where this challenge looks. The charge is made here.
20–220
beam energy, MeV
0.01–1.5
bunch charge, nC
0.833–10
repetition rate, Hz
1–150
bunches per train
Forecasting the CLEAR beam charge
03
Notes: CLEAR is a roughly 40 m electron linac at CERN, run as a user facility since 2017. A laser hits the photocathode in the RF gun, which produces and accelerates the electrons. The accelerating structures, fed by two klystrons, MKS11 and MKS15, then take the beam to the experimental areas. This challenge looks at the start of the machine, where the charge is made.

## Slide 4: Where the charge is made
THE INJECTOR
Laser lab
lab_laser_power
Transport line
clex_laser_power
laser_scope
Virtual cathode
BTV0125 camera
Gun RF
PGIA PGRA PGLA PGIP
RF gun
with the photocathode
Solenoids
SNH_110 SNI_120
Corrector
DHG0130
Charge
BCM_GUN
to the linac
Hall: TEMP1–4, HUMID1–4
Forecasting the CLEAR beam charge
04
Notes: A closer look at where the charge is made, and where each recorded signal sits. The laser energy is measured twice, in the laser lab and in the accelerator, and a fast photodiode sees each pulse. A mirror sends part of the laser to the virtual-cathode camera, BTV0125, which shows the spot as the cathode sees it. The rest hits the photocathode inside the RF gun, powered by the gun RF. The electrons then pass two solenoids and a corrector, and BCM_GUN measures their charge. The hall temperature and humidity are recorded too. The drawing is schematic, not to scale.

## Slide 5: Three steps, one question
THE CHALLENGE
STEP 1 · EASY
Understand
raw run → clean table
Clean, synchronise, rank every signal.
STEP 2 · MEDIUM
Virtual diagnostic
Q[t] = f(X[t])
This shot's charge from this shot's signals.
STEP 3 · HARD
Forecast
Q[t+1…t+H] = f(X[≤t], Q[≤t])
The next shots' charge, from the past.
THEN, OPTIONAL
Close the loop with a controller g(x) on laser power or RF phase. Extremely promising results can earn real beam time on CLEAR.
Forecasting the CLEAR beam charge
05
Notes: The parent challenge asks how to find the best settings. This one adds time: how will the beam behave next? Three steps, which are also the three tiers. First understand the data. Then a virtual diagnostic: the charge of a shot from the other signals of the same shot. Then forecasting: the charge of the next shot, or several shots ahead, from the past only. The long-term goal is to put the forecast inside a controller, which brings us back to optimisation. And if a team gets extremely promising results, we can ask for real beam time to test it on CLEAR.

## Slide 6: Studied, but still under development
A first study showed the approach works. It is not finished: forecasting is still being developed.
Task | Best MAE, pC | Note
Virtual diagnostic | 3.37 – 6.56 | R² 0.56 – 0.84
One-step forecast | 4.12 – 7.47 | best: TFT, XGBoost, DeepAR
Rolling mean, no model | 4.28 – 7.73 | the naive baseline
Forecasts lean on the charge's own past. Laser and RF help, but much less.
For this challenge, custom datasets were acquired, and they are shared with you.
Forecasting the CLEAR beam charge
06
Notes: This topic is not new for us: we presented a first study at MaLAPA in April 2026. The virtual diagnostic worked well. Forecasting was much harder: the best models, TFT, XGBoost and DeepAR, only just beat a plain rolling mean, and the forecasts leaned mostly on the charge's own past. So this is still under development, and that is exactly where you come in. For this challenge we acquired new, custom datasets, and they are shared with you.

## Slide 7: Beat the rolling mean.
A GOOD FIRST EXERCISE
Predict each shot as the mean of the last 9 good shots. It is surprisingly hard to beat.
Forecasting the CLEAR beam charge
07
Notes: A good first exercise for the Hard tier: beat the rolling mean. Predicting each shot as the average of the last nine good shots is a very strong baseline for this signal. On the earlier data the best models only just beat it. But this is new data, taken under different conditions, so don't draw conclusions from those numbers: find out for yourselves.

## Slide 8: Many runs, many machine conditions
THE DATA · OCTOBER 2026
The runs were taken on purpose under different conditions. None is labelled: recognising each one is part of the challenge.
Stable operation
A steady machine: the cleanest case.
Saturation
Wrong conditions: little or no correlation to find.
Single and multi-bunch
One bunch per shot, or a whole train.
Laser scans
Laser position and/or intensity varied during the run.
Not every run will be useful for training. Every run will test your processing.
Forecasting the CLEAR beam charge
08
Notes: The data was acquired on CLEAR in October 2026, specifically for this challenge. The runs are deliberately diverse and represent real operating conditions: stable operation, runs in wrong conditions such as saturation where you should not expect much correlation, single and multi-bunch beams, and runs where the laser position or intensity was varied. Nothing is labelled. Some runs may not be useful for training a model at all, but every one of them is a good test of your processing.

## Slide 9: 23 parameters in six families
WHAT IS RECORDED
Charge · target
BCM_GUN
beam charge at the gun, nC
Laser
lab_laser_power clex_laser_power laser_scope BTV0125
energy in the lab and in the linac (J), a fast photodiode, the virtual-cathode camera
Gun RF
PGIA PGRA PGLA PGIP
incident and reflected power, gun loop, phase; 960-sample waveforms
Klystron 15
PKI15A PKR15A PKI15P
incident and reflected power, phase; 960-sample waveforms
Magnets
SNH_110 SNI_120 DHG0130
solenoid and corrector currents, A; slow
Ambient
TEMP1–4 HUMID1–4
hall temperature and humidity; slow
Not every signal carries information. Finding out which ones do is part of the challenge.
Forecasting the CLEAR beam charge
09
Notes: Every shot records 23 parameters: the target charge BCM_GUN, the laser seen four ways, the gun RF, klystron 15, three magnets and the hall conditions. The RF signals are in arbitrary units, so compare them within a run, not across runs. And an important point: we do not promise that every signal is useful. Some may be redundant, some may be noise. Saying "this signal tells us nothing", with evidence, is a valid result.

## Slide 10: Real machine data
WHY IT IS HARD
Every reading has its own clock
A device that has not updated yet hands over the previous shot. Put each reading back on its shot.
Slow devices
Temperature, humidity and magnet currents update less than once per shot.
Bad shots
Charge dropouts, bad camera exposures, a saturated scope. Flag them, don't delete them.
Features to build
Waveforms and camera images must become numbers: peaks, integrals, windows, spot position.
Forecasting the CLEAR beam charge
10
Notes: This is not a clean benchmark. Each value comes with its own acquisition stamp, and a device may still be showing the previous shot, so synchronisation is real work. Some devices update far less often than once per shot. There are charge dropouts and bad camera frames: flag them, because forecasting needs them later. And the RF waveforms and camera images have to be turned into features first: which part of a waveform, which property of the laser spot, actually matters?

## Slide 11: Understand and clean the data
TIER 1 · EASY
Clean the raw run, and grasp understand of all of them in which conditions were acquired and what they mean
Work out each run's regime from the data
Flag dropouts and bad shots; don't delete them
Put every reading back on its own shot
Go beyond a waveform's peak and integral
Rank every signal four ways: Pearson, Spearman, distance correlation, mutual information
THE GOAL
Synchronize the data checking different at lags for different variables
A reason for every variable kept or dropped
A ranking that holds across runs, or is explained where it changes
Prepare dataset for the future test
Forecasting the CLEAR beam charge
11
Notes: Easy is about understanding. Clean a run, put every reading back on the shot it belongs to, and find out which variables really carry information about the charge. A good check for synchronisation: after alignment, a laser signal's dark shots should line up with the charge dropouts at lag zero. The kickoff notebook, sections 2 and 3, does a first pass, including a noise floor that tells real correlations from chance.

## Slide 12: Virtual diagnostic
TIER 2 · MEDIUM
Examinate the performance of various model and try with and without BCM_GUN in the loop
Compare a linear model, a tree ensemble and a neural network
Show what drives each model
Cross-run: train on one run, test on another
Report how much the metrics change with different past history
THE GOAL
Obtain good performance in the virtual diagnostic fashion.
Identify the right metric and try some basic model (ElasticNet, Random Forest, XGBoost and MLP).
Forecasting the CLEAR beam charge
12
Notes: Medium is the virtual diagnostic: infer the charge of a shot from the other signals of that same shot, without using any charge. Compare at least a linear model, a tree ensemble and a neural network, and show what drives each one: does it agree with your correlation study? Then the interesting part: train on one run and test on another, across days or across regimes. How much does it degrade, and which features stop transferring?

## Slide 13: Forecasting
TIER 3 · HARD
Repeat what done for virtual diagnostic in a more complex scenario
One step ahead, then up to 50 shots
At least one sequence model: TFT, DeepAR, LSTM/GRU or a time-series foundation model
Tune the context window and show its effect
THE GOAL
Identify the right metric and try some basic model
Beat the rolling mean
Deploy in the machine the model
Forecasting the CLEAR beam charge
13
Notes: Hard is forecasting: predict the charge of future shots from everything known up to now. First beat the rolling mean, which is not trivial. Then beat the notebook's XGBoost on lag features. Go multi-step and find the horizon where your model stops beating the rolling mean. Use at least one model built for sequences. And tell us where the forecast comes from: the charge's own history, or the machine.

## Slide 14: Same rules for every team
SCORING
Chronological split
Test on the last 10 % of each run. No shuffling; fit everything on the first 90 %.
Metric in nC
Try different and understand their physical meaning.
Dropouts not scored
Charge below 30 % of the local median.
Decomposition
Careful in the approach to be sure to be leakless
Forecasts
Complex problem try feature engineering
Ranking
Try different model and rank them by performance
Forecasting the CLEAR beam charge
14
Notes: The rules are fixed in score.py, so every team is scored the same way. The split is chronological: the last 10 % of each run is the test region, and nothing is shuffled. The score is MAE in nanocoulombs. Charge dropouts are not scored, but shots with a device flag are, because their charge is real. Report every scored run, not your best one. For forecasting, also report the gain over the rolling mean. Ranking is the highest tier with a bar beaten, ties broken by that tier's MAE.

## Slide 15: Build your own pipeline
GETTING STARTED
The kickoff notebook shows one way through the three tiers. Take it as an example, not a recipe: you are free, and encouraged, to develop your own analysis.
Shown in the kickoff notebook
Reducing a run to one row per shot
Quality checks, dropouts, synchronisation
A first correlation study
Baseline models for some tier
Up to you
Your own cleaning and synchronisation
Your own features from waveforms and images
Any model you can justify
Extras: frequency bands, uncertainty, closing the loop
Forecasting the CLEAR beam charge
15
Notes: The kickoff notebook will show you one way through: reducing the raw data to one row per shot, the quality checks and synchronisation, a first correlation study, and baseline models for each tier. Use it as an example, not as a recipe. We strongly encourage you to build your own analysis pipeline: your own cleaning, your own features, any model you can justify. The only thing fixed for everyone is the scoring, so results stay comparable. Everything is in the forecasting folder of the optimisation challenge.

## Slide 16: Let's predict the next shot
THANK YOU
Questions now, or any time this week.
Antonio Gilardi
antonio.gilardi@cern.ch
Notes: That is the challenge: understand the data, infer the charge, then try to predict the next shot. Questions now, or any time during the week: find me at the Tuesday hands-on session or the Wednesday check-in.